## Slide 1: Challenge on Multicast
Louis Chan
Network Consultant - Asiapac
email: lchan@unispherenetwork.com

## Slide 2: Multicast Overview
Why Multicast
  Conserve bandwidth
  Reduce network equipment load
  Reduce server load
  Reduce peering requirement
Unicast would require that the source host send a duplicate packet to every receiver
Multicast requires the source host to send a single packet and the network takes care of replicating the packet for multiple receivers
Application
  multimedia distribution, games, real time information, conferencing

## Slide 3: Multicast Drawback
Unreliable mechanism
  sender does not know whether all receivers get the packet.
  need application support
  may require network design to provide redundant information
Possibility of duplicate packet/stream
  multiple path co-exist at some time
Increase chance of network congestion

## Slide 4: Protocols
IGMP & IGMP Proxy
PIM-SM, PIM-DM, PIM S/D
DVMRP
MOSPF
MBGP
Others..
  MSDP
  BGMP
  MASC

## Slide 5: Multicast Topology
Multicast forwarding state is maintained in the form of (S,G) entries
  (S,G) multicast entries are similar to unicast route entries
Reverse Path Forwarding (RPF) check
  Multicast protocols use RPF check to ensure that data is only accepted from the interface which leads to the best path back to the source
Routing table has 2 views:
  Unicast usable routes – these routes are learned via unicast routing protocols (RIP, OSPF, IS-IS, etc.) and then used for forwarding unicast data
  Multicast usable routes – these routes are learned via unicast routing protocols (RIP, OSPF, IS-IS, etc.) and multicast routing protocols (DVMRP & MBGP) and then used for forwarding multicast data
Not all of the routers in the network need to run multicast
  Some portions of the network are completely isolated from multicast traffic
  Connect isolated multicast segments by tunnelling through non-multicast capable routers using GRE, DVMRP tunnels

## Slide 6: Sparse Mode vs Dense Mode Protocols
Sparse mode
  Focused on limited distribution
  Hosts must explicitly send IGMP group joins to receive multicast data
  Assumes that those who want data will request it (join)
  Once you’ve joined, you must explicitly leave multicast group to stop receiving data
  Routers maintain (source, group) state info
  Rendez-vous point (RP) or core needed for learning sources
  e.g. PIM SM
Dense mode
  Focused on wide distribution
  Hosts must explicitly send IGMP group joins to receive multicast data (they get the 1st packet automatically)
  Assumes that routers without local group members (local hosts that receive 1st packet but don’t join) will complain (prune)
  Once you’ve joined, you must explicitly leave multicast group to stop receiving data
  State info maintained for each source at every router in the network
  e.g. PIM DM, DVMRP
The aim is to build the distribution tree!

## Slide 7: Example - PIM-DM/ IGMP Operation
R2
R4
R5
R7
R8
R3
R9
IGMP R3
- G1
IGMP R7
- G1
PIM R3
PIM R2
PIM R5
- (S1,G1)
Source S1
- (*,G1)
- (S1,G1)
- (S1,G1)
PIM R8
- (S1,G1)
G1 Data
G1 Data
G1 Data
G1 Data
G1 Data
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Challenge - Performance
Broadcast Multiaccess environment - e.g. ethernet
  one copy per segment
Non-broadcast Multiaccess environment - e.g. xDSL, wireless, LL
  one copy for each

## Slide 9: Challenge - Performance
Traffic volume
  video take 100kbps to 4Mbps bandwidth in practice
  relatively huge number of subscriber in NBMA environment
Buffer and Memory Management
Software implementation for duplication of packet
Hardware assisted duplication

## Slide 10: Challenge - Streaming Requirement
Steady multicast stream
  jitter cause instantaneous congestion
  buffer requirement at client application

## Slide 11: Challenge - Implementation issue
Multicast does not support authenication
  no authenication in IGMP. IGMP V3 only allow you to select source to join
  encryption method - key distribution problem
  use other method for the CAC control
Traffic engineering issue
  redundancy & load sharing
  multicast only accept one ingress interface

## Slide 12: Quality of Service
How to maintain QOS
Replicate multicast traffic close to subscriber

## Slide 13: Quality of Service
Separate the domains
Unicast
Domain
(Best Effort)
Internet
Multicast
Domain

## Slide 14: Quality of Service
via virtual router
Internet
Multicast
Domain
Unicast
Domain
(Best Effort)

## Slide 15
Any Questions?