## Slide 1: APRICOT 2011 Hong Kong Network Security Workshop
Alastair JOHNSON alastair.johnson@alcatel-lucent.com
Jonny MARTIN jonny@pch.net
Tony CHAN tonychan@juniper.net
19 February 2011
Notes: <number>

## Slide 2: Some Simple Best Practices
  Always null route unused address space within your network
    If you have prefixes you know are unused, route them towards null0 on your routers.
    Prevents ARP cache exhaustion, broadcasts, and prevents address theft
  Enable port security and limit the number of MACs on customer ports
  Always filter ingress traffic from customers with uRPF or ACLs (source address validation)
  Authenticate all of your network protocols
  Filter BGP sessions ingress and egress
    Make sure you don’t accept prefixes you don’t want or shouldn’t carry
  Set maximum-prefix/prefix-limit on BGP sessions (including customers, transits, and peers)
  Never use OSPF as a CE-PE protocol

## Slide 3: Some Simple Best Practices
  Give high priority to network control traffic
  Ideally, have an out-of-band management path to all POPs.
  Restrict DHCP and Router Advertisements on customer ports
  Separate customers into separate VLANs if you can
  Use local-proxy-arp and private VLANs to restrict device-to-device communications
  Use an anomaly detection system – even if it’s just netflow and a suspicious eye!
  Use RANCID or similar to monitor configuration changes on network elements.
  Ensure you are logging to central locations via syslog / SNMP traps.
  Monitor critical network element resources, e.g. memory, bandwidth utilisation, interface utilisation, RIB/FIB utilisation, CAM utilisation…

## Slide 4: Some Simple Best Practices
  ALWAYS ENCRYPT YOUR MANAGEMENT TRAFFIC!
    Avoid the use of clear text as much as possible.
    Limit clear text traffic to the shortest and most trusted path possible.
  Make use of jump or bastion hosts and ACLs to restrict management traffic to these hosts.
  Have a security plan that includes incident management processes
    Identify who, what, and how
    Practice and test the plan
    Make sure you know how to reach your peers and transit providers, and how their security plans work!
  Join security working groups such as NSP-SEC.
  Keep an eye on mailing lists like NANOG, PacNOG, APOPS, Bugtraq, Full-Disclosure.

## Slide 5: Some Simple Best Practices
  Use least-privileged mode where possible
    If you’re logging in to check interface stats, you probably don’t need superuser mode.
    Define profiles for staff that restrict them to the appropriate privilege level.
  Keep on top of OS releases for your network elements, particularly if security patches are released.
    ACLs and Control Plane Policing can mitigate this, to an extent.
  When implementing IPv6, be careful and ensure that your ACLs, filters, CoPP, etc incorporate the fact that all protocols will start listening on the IPv6 addresses.
  Don’t block all ICMP – there are some really important parts of it.
    Question: What can break when ICMP is blanket-blocked?

## Slide 6: Some security references
  ITU X.805
  ISO 15408 Common Criteria
  ISO/IEC 27001
  Team Cymru – http://cymru.org
  An interesting look at leaky ISPs at IXPs – Monkeying Around on the APE
    http://www.apricot.net/apricot2010/__data/assets/pdf_file/0006/18915/IXPs_02_Monkeying-around-on-the-APE_Mike-Jager.pdf
  Grab anything you want to refer to from http://192.168.175.1
  Feel free to ask the instructors or contact us!

## Slide 7: Some tools we used this week…
  tcpdump – http://www.tcpdump.org
  Wireshark – http://www.wireshark.org
  Cacti – http://www.cacti.net
  Scrutinizer (Netflow tool) - http://www.plixer.com
  Perl Net::RawIP tools for generating attack traffic
  Ettercap – http://ettercap.sourceforge.net
  Yersenia – http://yersinia.net
  nmap – http://nmap.org
  Good old ping - on a unix host near you
  Nessus – http://nessus.org

## Slide 8: Quiz! (1/73)
When would you use telnet to manage devices?
What’s the first thing you do to usernames and passwords on new equipment?
What size is Jonny’s puku?
Why is it important to have NTP configured?
Is SYSLOG traffic clear-text or encrypted?
Why must you authenticate routing protocols? (at least 3 reasons!)
What filters should you include at a minimum on eBGP sessions?
Why should you use maximum-prefix / prefix-limit on BGP sessions?
What interfaces should OSPF never be run on?
What BCP should you be familiar with and implement? Why?

## Slide 9: Quiz! (2/73)
What’s a bogon (or martian)?
Should bogons be in your filtering list? Give an example.
Give some example of filtering techniques
What’s the advantages of RTBH over ACLs or filters?
What is Tony’s middle name?
What signalling protocol does RTBH use?
What is the advantage of Source Based (S/RTBH) over Destination Based (D/RTBH)?
Why must you configure uRPF?
Where should you always configure uRPF?
Explain the difference between strict and loose uRPF.

## Slide 10: Quiz! (3/73)
Can we have your private SSH keys?
Give an example of where you’d use a sink hole
Name three network telemetry tools or protocols
Explain what a flow is
What’s the difference between a hardware based and software based router?
How is Control Plane Policing (CoPP) useful?
What CoPP traffic should not be policed/rate-limited?
Does MPLS secure customer traffic?
What should the infrastructure ACL primarily protect?
Is it a good idea to assign your loopback addresses from a simple aggregate?

## Slide 11: Quiz! (4/73)
What basic security measures should be placed on every user-facing L2 port?
What types of hat do attackers wear?
What does ARP do? Bonus point: what replaces ARP in IPv6?
What is ARP poisoning?
What information does a switch use to protect against IP spoofing?
Name a type of DHCP attack
Is spanning-tree a good idea?
Is your lab pod secure?
Why would you use AAA to authenticate router logins?
Name two AAA protocols
Who has the better mustache?

## Slide 12: Quiz! (5/73)

## Slide 13
www.alcatel-lucent.com
www.apricot.net
www.alcatel-lucent.com