## Slide 1: Loopback Filter Policing
Tony Chan
18 Feb 2011

## Slide 2: Loopback Filter policing
Config firewall filter
Config policer
Apply filter to lo0 ingress

## Slide 3: ARCHITECTURE
lo0
Routing Engine
FPC
0
FPC
n
0
1
2
3
0
1
2
3
IP II
Input
Output
Packet
Forwarding
Engine
Transit Traffic
Control Traffic
e.g. BGP/OSPF
Transit Traffic
Apply Filter/Policer here to protect RE!

## Slide 4: config firewall Filter
firewall {
family inet {
filter PROTECT-RE {
term ICMP-DOS-PREVENTION {
from {
source-prefix-list {
1.1.1.1/32;
}
protocol icmp;
}
then {
policer RE-LOW-POLICER;
}
}

## Slide 5: Config Policer
firewall {
policer $policer_name$ {
if-exceeding {
bandwidth-limit $bandwidth_limit$;
burst-size-limit $burst_size$;
}
then discard;
}

## Slide 6: Common PoLice Rate
Policer | bandwidth-limit | burst-size-limit
RE-LOW-POLICER | 50k | 15k
RE-MEDIUM-LOW-POLICER | 500k | 64k
RE-MEDIUM-HIGH-POLICER | 1m | 128k
RE-HIGH-POLICER | 20m | 256k

## Slide 7: Apply filter to lo0
lo0 {
unit 0 {
family inet {
filter {
input protect-re;
}
address 10.1.1.1/32;
}
}
}

## Slide 8: For more info...
For more informations:
http://www.juniper.net/techpubs/software/jseries/junos90/jseries-config-guide-advanced/configuring-a-routing-engine-firewall-filter-for-services-and-protocolsfrom-trusted-sources.html#configure-services-protocols-sources-firewall-section
http://www.juniper.net/techpubs/software/jseries/junos90/jseries-config-guide-advanced/configuring-a-routing-engine-firewall-filter-to-protect-against-tcpand-icmp-floods.html#configure-flood-firewall-section
http://www.juniper.net/techpubs/software/jseries/junos90/jseries-config-guide-advanced/configuring-a-routing-engine-firewall-filter-to-handle-fragments.html#configure-fragments-filter-section

## Slide 9
Notes: 9