## Slide 1: APRICOT 2011 Hong Kong Network Security Workshop
Alastair JOHNSON alastair.johnson@alcatel-lucent.com
Jonny MARTIN jonny@pch.net
Tony CHAN tonychan@juniper.net
16 February 2011
Notes: <number>

## Slide 2: Filters
  Like Cisco ACLs
  Applicable to L2 (MAC) and L3 (IPv4/IPv6) - 65K filters available, identified by 1-65535.
    config>filter>mac-filter
    config>filter>ip-filter
    config>filter>ipv6-filter
  Apply filters to interfaces:
    configure router interface “to-INTERNET” ingress filter 101
    configure service ies 1234 interface “to-CUSTOMER” egress filter 234
    match
    dst-ip, src-ip, ports, etc
    action
    forward [next-hop] or drop
    log
  filter
  ip-filter 101 create
  entry 10 create
  description "match evil bits"
  match
  src-ip 127.0.0.0/8
  exit
  action drop
  exit
  entry 20 create
  description "permit other traffic"
  match
  exit
  action forward
  exit

## Slide 3: Management Access Filters
  Control traffic to the CPM and should be configured to permit routing protocols and management traffic as a ‘fine tuning’ filtering.
  Software based – use cpm-filters for hardware filtering.
Router>config>system>security# info
----------------------------------------------
management-access-filter
default-action deny
entry 1
action permit
src-ip 10.10.99.104/32
exit
entry 2
action permit
src-ip 10.10.89.1/32
exit
exit

## Slide 4: CPM Filters
  Hardware based CPM filters
  Router>config>system>sec>cpm>ip-filter# info
  ----------------------------------------------
  entry 10 create
  description ”CPM-Filter 10.10.101.3 #101”
  log 101
  exit
  entry 20 create
  description ”CPM-Filter 10.10.101.3 #201”
  log 101
  exit
  no shutdown
  ----------------------------------------------

## Slide 5: Control Plane Queues
  8000 queues available on the CPM for ingress CPM-destined traffic.
    Queue 1-8 default queues (can’t be changed, per standard FCs)
    Queues 33-2000 can be allocated based on CPM ingress filters.
    Queues 2001-8000 per peer queuing
      configure system security per-peer-queuing
  Implements per peer queuing with a round-robin scheduler (BGP/LDP)
    Ensures that peers cannot starve or congest the CPM.
  Unclassified traffic will match the standard queues.

## Slide 6: CPM Filters with Queues
  Router#configure router system security cpm ip-filter
  Router>config>system>security>cpm-filter>ip-filter# info
  --------------------------------------------
  entry 10 create
  description ”Match SSH traffic from NOC”
  match src-ip 192.0.2.0/24
  match dst-port 22
  match protocol tcp
  action queue 33
  exit
  entry 20 create
  description ”Match all ICMP traffic”
  match protocol icmp
  action queue 34
  exit
  no shutdown
  ----------------------------------------------
  Router#configure router system cpm-queue 33 create rate 128
  Router#configure router system cpm-queue 34 create rate 1024

## Slide 7: CPU Protection
  Allows per protocol packet rate limits for traffic that is punted to the CPM
    OSPFv2/v3, IS-IS, RSVP-TE, LDP, RIP, PIM, MLD, IGMP, BGP, BFD, L2PT, PPP, DHCP
    3 color marking QoS profile
  Global configuration options:
    link-specific-rate – applies to link-level protocols and is per link
    port-overall-rate – applies to all control traffic per port.
    protocol-protection – blocks traffic for unconfigured protocols.
  CPU Protection Policies
    overall-rate – applies to all control traffic (all sources) received per interface.
    per-source-rate – applies to all control traffic received per source (e.g. per MAC)
    out-profile-rate – applies to all control traffic on an interface. Traffic above this rate will be marked discard eligible (DE).
  Two default policies
    254 is the default for access interfaces
    255 is the default for network interfaces

## Slide 8: CPU Protection
Router>config>sys>security>cpu-protection# info
----------------------------------------------
link-specific-rate 4000  4000 pps max
policy 4 create
no alarm
description "My new CPU Protection policy"
overall-rate 9000  9000 pps max
per-source-rate 2000  2000 pps
out-profile-rate 4000  above 4000 pps, packets are marked out-of-profile
exit
policy 254 create
exit
policy 255 create
exit
port-overall-rate 12000  12000 pps for all traffic per port
protocol-protection
----------------------------------------------
Router>config>service>ies>if# info
----------------------------------------------
cpu-protection 4
sap 1/1/5 create
exit
----------------------------------------------

## Slide 9
www.alcatel-lucent.com
www.alcatel-lucent.com